## Slide 1: Discrete TRENCHSTOP™ IGBT7 family
Infineon Technologies
September 2025

## Slide 2
Agenda
Commercial overview
Technology background
5 values of discrete IGBT7 family
Key takeaways and resources
1
2
3
4
Notes: Decisive 5 Values

## Slide 3
Comercial overview

## Slide 4: It´s time to Switch! 5 Decisive Values of TRENCHSTOPTM IGBT7 family
Value Proposition
Space minimization or increased output power for the same system size
Power Density
First time Infineon offer Power discrete devices up to 140 A for 1200 V and up to 150 A for 650 V and 750 V
More output current, lower case temperature
Efficiency
Lowest power losses compared to previous generation
Best system performance and good price/performance ratio
System cost
Bridging the gap between traditional silicon IGBTs and offering a cost-effective alternative to wide-bandgap solutions
Extra reliability, even in high-humidity environment
Quality
Qualified by standard for HV-H3TRB
One family to fulfill the overall power application needs
Ease of Use
Easy to switch, fine controllability with a rugged transient. Flexible family to replace most predecessor technologies. 61 Products in 7 different packages
Customer benefits
Product features
650 V
3 A
…
150 A
Voltage Class
Current Class
2 – 100 kHz
Switching Frequency
1200 V
Link to 5 Decisive Values of IGBT7 report!
www.infineon.com/discreteIGBT7
750 V

## Slide 5: Product vision
3 voltage classes 650 V, 750 V & 1200 V
3 flavors T7, H7 & S7
7 packages
61 products
Benchmark performance
with state-of-the-art quality and best price/performance ratio
IGBTs Produced in a newest fully-automated 300mm chip factory
Manufacturing footprint
Flexible family
to replace almost all predecessor technologies

## Slide 6
Generation
Storage and transmission
Consumption
Solar
UPS
Energy storage systems
Fuel cell
Heat pump
EV Charging
CAV
H7
Fulfill the overall energy chain needs
H7
S7
H7
S7&T7
T7
H7
H7
S7&T7
Drives
TRENCHSTOP™

## Slide 7: TRENCHSTOP™ IGBT7 – 650 V, 750 V and 1200 V H7
3 voltage classes
650 V
750 V
1200 V
5 packages
IKWH
IKW
IKZA
IKQ
IKY
H7 technology offers uncompromising performance and full utilization of it´s capabilities
40 A | 50 A | 75 A | 100 A | 120 A | 140 A | 150 A
Supreme Performance
38 products
H7

## Slide 8: TRENCHSTOPTM IGBT7 H7 family for solar, ESS and EV charging applications
 | Current Inom | TO-247-3-HCC high creepage, high clearance | TO-247-3 | TO-247-4pin asymmetric | TO-247PLUS-3pin | TO-247PLUS-4pin
650 V | 40 A | IKWH40N65EH7 |  | IKZA40N65EH7 |  | 
 | 50 A | IKWH50N65EH7 |  | IKZA50N65EH7 |  | 
 | 75 A | IKWH75N65EH7 |  | IKZA75N65EH7 |  | 
 | 100 A | IKWH100N65EH7 |  | IKZA100N65EH7 |  | 
 | 120 A |  |  |  | IKQ120N65EH7 | IKY120N65EH7
 | 150 A |  |  |  | IKQ150N65EH7 | IKY150N65EH7
750 V | 50 A | IKWH50N75EH7 |  | IKZA50N75EH7 |  | 
 | 75 A | IKWH75N75EH7 |  | IKZA75N75EH7 |  | 
 | 100 A | IKWH100N75EH7 |  | IKZA100N75EH7 |  | 
 | 120 A |  |  |  | IKQ120N75EH7 | IKY120N75EH7
 | 150 A |  |  |  | IKQ150N75EH7 | IKY150N75EH7
1200 V | 40 A |  | IKW40N120CH7 | IKZA40N120CH7 |  | 
 | 50 A |  | IKW50N120CH7 | IKZA50N120CH7 | IKQ50N120CH7 | IKY50N120CH7
 | 75 A |  | IKW75N120CH7 | IKZA75N120CH7 | IKQ75N120CH7 | IKY75N120CH7
 | 100 A |  |  |  | IKQ100N120CH7 | IKY100N120CH7
 | 120 A |  |  |  | IKQ120N120CH7 | IKY120N120CH7
 | 140 A |  |  |  | IKQ140N120CH7 | IKY140N120CH7
New Release: October 2025

## Slide 9: TRENCHSTOPTM IGBT7 H7 family for solar, ESS and EV charging applications
40 A
Value Proposition
Maximize system output power
Power Density
Highest power density, first on the market with 140A rating in 1200V and 150A for 650 V and 750 V discrete devices
Uncompromising performance and full utilization
Efficiency
Best in class conduction and switching power losses performance
Best system performance and good price/performance ratio
System cost
A cost-effective alternative to wide-bandgap solutions
Extra reliability, even in high-humidity environment
Quality
Qualified by JEDEC standard for HV-H3TRB
Uncompromising performance and full utilization
Ease of Use
Easy to switch, developed to fulfill the demand in green energy and efficient applications
Customer benefits
Product features
650 V
Voltage Class
16 – 100 kHz
Switching Frequency
1200 V
Current Class
140 A
750 V
50 A
100 A
120 A
75 A
150 A

## Slide 10: TRENCHSTOP™ IGBT7 – 650 V and 1200 V T7/S7
2 voltage classes
650 V
1200 V
5 packages
23 products
T7/S7
T7 and S7 technology is the ultimate choice for robust performance and precise control with a Short Circuit Withstand Time (3-8µs)
3A | 8 A | 15 A | 20 A | 25 A | 30 A | 40 A | 50 A | 75 A | 100 A | 120 A
IKW / IGW
IKZA
IKQ / IGQ
IGD
IGB
Short Circuit Robustness

## Slide 11: TRENCHSTOPTM IGBT7 T7/S7 family for applications where short circuit is required (e.g. Motor Drive)
 | Current Inom | TO-252-3-11 DPAK | TO-263-3-2 D2PAK | TO-247-3 | TO247PLUS-3pin Copacked with full rated diode | TO247PLUS-3pin Single IGBT
650 V | 20 A |  |  | IKW20N65ET7 |  | 
 | 30 A |  |  | IKW30N65ET7 |  | 
 | 40 A |  |  | IKW40N65ET7 |  | 
 | 50 A |  |  | IKW50N65ET7 |  | 
 | 75 A |  |  | IKW75N65ET7 |  | 
1200 V | 3 A | IGD03N120S7 | IGB03N120S7 |  |  | 
 | 8 A | IGD08N120S7 | IGB08N120S7 | IKW08N120CS7 |  | 
 | 15 A |  | IGB15N120S7 | IKW15N120CS7 |  | 
 | 25 A |  |  | IKW25N120CS7 |  | 
 | 40 A |  |  | IKW40N120CS7 |  | 
 | 50 A |  |  | IKW50N120CS7 |  | 
 | 75 A |  |  |  | IKQ75N120CS7 | IGQ75N120S7
 | 100 A |  |  |  | IKQ100N120CS7 | IGQ100N120S7
 | 120 A |  |  |  | IKQ120N120CS7 | IGQ120N120S7

## Slide 12: TRENCHSTOPTM IGBT7 T7/S7 family for applications where short circuit is required (e.g. Motor Drive)
Value Proposition
Minimize system design size
Power Density
3A-15A in small DPAK and D2PAK or up to 120A in TO-247PLUS package
More output current, lower case temperature
Efficiency
Lowest power losses across short-circuit rated devices
Best system performance and good price/performance ratio
System cost
The ultimate choice for robust performance
Extra reliability, even in high-humidity environment
Quality
Qualified by JEDEC standard for HV-H3TRB1
Ease of design for EMI compliance
Ease of Use
Fine controllability with a rugged transient.
Short circuit withstand time 3 - 8µs
Customer benefits
Product features
650 V
2 – 20 kHz
Switching Frequency
1200 V
Current Class
40 A
3 A
100 A
120 A
T7
S7
8 A
15 A
20 A
25 A
50 A
75 A
1DPAK/D2PAK portofilo has H3TRB qualification only

## Slide 13: IGBT7 manufacturing footprint
The world's first production of power semiconductors in 300-millimeter thin wafer technology
These particularly thin energy-saving chips ensure even more efficient energy conversion in electronic systems.
Villach
Dresden
R&D
Production
Global business responsibility
IGBTs produced in the
newest fully automated
300 mm chip factory
One virtual fab: virtual mega-factory for 300-millimeter thin wafers together

## Slide 14: Emitter control 7 diodes

## Slide 15: 650 V emitter controlled 7 discrete diode
The same diode is copacked with
650 V IGBT7 H7 and T7
Notes: 9 products

## Slide 16: 1200 V emitter controlled 7 discrete diode
The same diode is copacked with
1200 V IGBT7 H7
Notes: 8 products

## Slide 17: 650 V emitter controlled 7 discrete diode

## Slide 18
Technology background
The two flavours of

## Slide 19: Industrial applications trade-off curves IGBT flavors for different applications and voltage classes
Conduction Losses
[Vce(sat)]
Switching losses
[Etot]
<= Low switching 20 kHz
Fast switching up to 20-100 kHz =>
650V
S7
H7
1200V
T7
H7
Short circuit rated
750V
H7

## Slide 20: Industrial applications trade-off curves Diode flavors for different applications and voltage classes
Conduction Losses
[VF]
Switching losses
[Qrr]
<= Low switching 20 kHz
Fast switching up to 20-100 kHz =>
ECS7
ECH7
1200V
Soft diode
Snappy diode

## Slide 21: Infineon´s TRENCHSTOP™ IGBT7 What is new
Dynamic performance | CGE | CCE | CCG
Active gates |  |  | 
Dummy gates |  |  | 
Emitter |  |  | 
Gates/Emitter ratio |  |  | 
Main Influence Secondary influence |  |  | 
Dummy gate
Emitter trenches
What is the Micro-Pattern-Trench (MPT)?
  Trench potentials designed for optimal capacitance behavior
Channel width engineering:
S7 balance short circuit and pulse-current requirements
H7 the steepest transfer characteristics
Channel distribution optimized for improved carrier confinement balancing:
VCE(sat) (main focus of S7)
Eoff (main focus of H7)
Notes: The proposed IGBT structure is based on micro-pattern trenches as shown in the top right corner drawing. In contrast to former Infineon technology, trenches can be utilized in several ways
As active channel  active gate
As dummy gate
As and emitter trenches
These three trench-cell building blocks allow tailoring the IGBT design, particularly the ratio active and dummy gate versus emitter trenches influence the capacitive coupling between collector and gate.
In the article mentioned, it has been demonstrated that the collector gate capacitance is mainly influencing the controllability, thereby the trade-off design of the Infineon IGBT7 S7 enhances softness during switching events maintaining low static losses and short circuit robustness.

## Slide 22: Infineon´s TRENCHSTOP™ channel width engineering
Larger
Thinner
Channel width
S7
H7
Saturation current needed
 Smoother transfer characteristics
 Short circuit withstand time
No saturation current needed
 Steeper transfer characteristic
 No Short circuit withstand time
  SCSOA rated IGBT has higher VCE(sat) and Ets than equivalent part with no SCSOA rating
Notes: The proposed IGBT structure is based on micro-pattern trenches as shown in the top right corner drawing. In contrast to former Infineon technology, trenches can be utilized in several ways
As active channel  active gate
As dummy gate
As and emitter trenches
These three trench-cell building blocks allow tailoring the IGBT design, particularly the ratio active and dummy gate versus emitter trenches influence the capacitive coupling between collector and gate.
In the article mentioned, it has been demonstrated that the collector gate capacitance is mainly influencing the controllability, thereby the trade-off design of the Infineon IGBT7 S7 enhances softness during switching events maintaining low static losses and short circuit robustness.

## Slide 23: 5 values of discrete IGBT7 family
Efficiency – „Optimization“
Power density – „Space Minimization“
System cost - „Affordability“
Ease of use – „Simplicity“
Quality – „Robustness“

## Slide 24: Ease of use – „Simplicity“
Easy to replace older technology
Controllability at its finest
Ruggedness in every condition

## Slide 25: Easy to replace older technology

## Slide 26: The never-ending debate: current density vs. thermal performance Can newer technology replace the older one?
S7 shows better performance (IoutMax)to T2 and H3.
The S7’s higher current density is perfectly compensated by the
lower static-dynamic losses.

Chart: Output current [A]
| 14.1 | 25.1 | 31 | 34.200000000000003
IKQ75N120CS7 Rg 6 ohm | 55.643 | 76.1 | 90.5 | 100.4
IKQ75N120CT2 Rg 6 ohm | 72.7 | 83.1 | 94.2 | 102
IKQ75N120CH3 Rg 6 ohm | 53.9 | 61.4 | 70.3 | 82.5 | 99.4
Parameter | Value | Unit
DC bus voltage | 800 | V
Modulation (SPWM) | 60 | %
Electrical frequency | 50 | Hz
Cos(phi) | 0.9 | -
Chip current density
R(th)JC goes higher
Do I get the same output power
Newer technology
Chip & system current density
Lower losses
Chip & system current density
Yes!
and even more!
How?

## Slide 27: Controllability at its finest

## Slide 28: Controllability and gate drive resistor selection
High Gate drive resistor Low
Low dV/dt High
High Dynamic losses Low
Low Insulation stress High
Requirement for GPD = 5 V/ns

Enlarged controllability
The worst-case-scenario current and temperature wise:
The turn-on gate resistor ensures that the event is within the limit at low current (5/10% of the nominal current) and room temperature.
The turn-off gate resistor ensures that the event is within the limit at nominal current and room temperature.
Notes: Why decrease the switching speed? Mainly to decrease stress in the machine insulation, due to voltage spikes.
How to do it? Increasing the gate drive resistor. Consequently the dV/dt slows down, but the total dynamic losses rise, especially during turn-on.
The dV/dt slope is also influenced by other boundary conditions, such as the collector current and device temperature. Thus, the selection of the turn-on gate resistor ensures that even at low current and low room temperature the event is sufficiently “soft”. While the turn-off gate resistor selection ensures that at nominal current and low room temperature the event is sufficiently “soft”.
The dV/dt of the devices under test are plotted in the figure and the gate resistances selection summarized in the table. As we can clearly see, fast trade of device as the one of the competitor X needs higher gate resistor to fulfill the requirement, while slower trade off components as the device of the competitor Y and the Infineon IKW40N120CS7 easily reach the goal with moderate magnitude.

## Slide 29: Ruggedness in every condition

## Slide 30: How to deal with short circuit withstand time?
The Infineon datasheet provides the short circuit current and withstand time as a function of gate-emitter voltage tSC = f(VGE) for the worst case of 150°C.
However, short circuit current ISC, consequently tSC, strongly depends on the bus voltage (VCC) and the Tvj as well.
Infineon already applies a ~25% safety margin in the tSC datasheet value!

## Slide 31: Parasitic turn-on performance Test results
Test conditions: dv/dt ~ 36 kV/us (low side) VCC = 800 V TJ = 175°C
PTO failure sample (competitor)
Qrr at RG_OFF HS = 0 
Qrr at RG_OFF HS = 47 
Err at RG_OFF HS = 0 
Err at RG_OFF HS = 47 
Diode recovery voltage, VF
dv/dt
IF
No Qrr and/or Err difference between
RG_OFF HS = 0  vs. 180 
Err
Diode recovery voltage, VF
36 kV/us
IF
No change in QRR/ERR
Clear change in QRR/ERR
RG_OFF HS

## Slide 32: Power density – „Space minimization“
Notes: Include ePA measurement

## Slide 33: Trends and challenges in paralleling
Why its important?
Increasing power density
Increasing output power
Reducing the risk
What are the challenges?
Static sharing
Dynamic sharing
How to solve?
Design
Symmetrical
Sorting
3L – NPC2
P
N
0
S1...Sn
S4...Sn
S3…Sn
S2…Sn
multi-phases
...
Notes: Before we jump into the power density and their outcome let’s have a deeper look into the system trends using discrete devices and how the IGBT7 address all the challenges in the design.
As the trend, we see more and more discrete devices are used in many applications by increasing the power density and output power. This trend is met in different ways, either by using high-current class devices and reducing the risk of paralleling or by paralleling and reducing the thermal stress on each device.
Symmetry in all Aspects – PCB design and Device parameters
With a symmetrical PCB design, we can avoid the issues of paralleling
Several parameters of the device will also play a crucial role

## Slide 34: Boost power density and enable size frame jump
Chart: Power density increase with the new large current classes in TO-247 PLUS
| 75 A | 100 A | 120 A
Power density Sil-Pad K10 | 50 | 60.5 | 73.68
Power density AL2O3-Keramik | 97 | 108 | 121
Reference: IKW40N120CS7
With Sil-Pad K10
Parameter | Value | Unit
VDC | 600 | V
Heat sink temp. | 100 | °C
Switching freq. | 6000 | Hz
Output freq. | 50 | Hz
Mod. index | 100 | %
Cos(phi) | 0.9 | -
Rg | As per datasheet value | -

Main value proposition driven by demand of increased power density:
Boost your power density up to:
~75% with the same thermal design
~120% with improved thermal design
Enabling enable frame-size jump
Boost up to 120%
power density
Notes: As we know power density is one of the main value proposition that all designers consider during their system design face, how the IGBT7 will help this? There where the high current density devices comes into play which results in having a high current class devices in the system. So here we have one of the examples showing the power density increase in drives application where the 40A 3pin is took as a reference in comparison to 75A, 100A and 120A devices where two different thermal interface materials are also evaluated with the standard boundary conditions for the drives as shown in the left. From this we can clearly see that using a 120A device we can boost upto 74% power density using silion pad and upto 120% using ceramic. Which clearly states that we can empower the system for higher power rating with the same system size.

## Slide 35: Internal and external fighting guide – TO-247 PLUS
Chart: Case temperature (output current) @ ~5 V/ns Sil-Pad® K-10 800Vdc fsw=10 kHz mindex= 0,7 fele=50 Hz cos(phi) ~ 0,9
| 17.3 | 21.3 | 25.8 | 31.2 | 34
IKQ75N120CS7 Rg 6 ohm | 61.2 | 68.3 | 78.2 | 91.3 | 100.3
2x 40A Competitor 1 Rgon 33 Rgoff22 | 71.4 | 76.1 | 79.8 | 84.2 | 88.1 | 93.4 | 97.8 | 103.4
2x 40A Competitor 2 Rgon 47 Rgoff 47 | 62.9 | 68.7 | 76.7 | 85.4 | 96.1 | 102.9
Size reduction
more power
TRENCHSTOP™ IGBT7
Increased power density
Size reduction more power

IGBT7:
Can replace 2 parallel 40 A rated devices from competitor
Notes: An another advantage of having higher current class devices is that we can reduce the risk of paralleling which was explained earlier which is also linked to the power density. In this graph you can see the outcome of 1 - 75A vs 2 – 40A devices of two different competitors where you clearly see the 75A IGBT7 can replace 2-40A devices from the competitor under the same test condition and also with the thermal interface material not only against competitor but also against pervious generation of IGBT from Infineon. In the end we can see that high current class devices of IGBT7 can helps in boosting the power density with higher performance. On the other hand its also wort to note that with higher current class devices there is also we brighter possibility to increase the output power of the system by having parallel device for eg. We can reach ~200kW with 4*140A in parallel.

## Slide 36: Efficiency – „Optimization“
Notes: Include ePA measurement

## Slide 37: Trade-off chart Key parameters – comparison
Chart: IGBT7 vs previous generation - VCE(sat) vs. ETOTAL
| 2
CH7 | 10.3
CS7 | 17.35
CH3 | 16.7
CS6 | 14.82
CT2 | 19.32
ET7 | 6.48
EH7 | 4.14
EL5 | 8.25
EH5 | 4.51
ES5 | 4.76
EH7 | 4.59
down to ~50% lower switching losses
down to ~20% lower conduction losses
Higher efficiency
Output power
Lower temperature
Micro-pattern-trench
Qrr vs VF
No saturation
*note – DUT – 75A 3pin devices
1200 V
650 V
750 V
H7 – 650 V
S5
H5
T7
H3
H7
S7
S6
L5
T2
H7 – 750 V
Notes: 650 V IGBT co-pack with EC7 Rapid Diode technologies shows better tradeoff performance versus previous generation IGBT5 - S5/H5
1200 V IGBT co-pack with EC7 Rapid Diode technologies shows better tradeoff performance versus previous generation IGBT – S6/H3 (with Short circuit withstand time)
Test condition for 650V– Vbus – 400V, Vge -0/15V, Rg – 10ohms, Temp – 175°C
Test condition for 1200V– Vbus – 600V, Vge -0/15V, Rg – 10ohms, Temp -175°C
In general, IGBT H7 shows lower Eon and higher Eoff losses, Resulting in lower total switching losses Ets for IGBT7 H7

## Slide 38: New vs. old technology
Chart: TO-247 3pin devices performance
| 0.48499999999999999 | 1.1870000000000001 | 1.6479999999999999 | 2.3370000000000002 | 2.7949999999999999 | 3.25 | 3.7029999999999998 | 4.3460000000000001
IKW40N120CH7 | 95.355 | 97.442 | 97.681 | 97.707 | 97.621 | 97.513 | 97.369 | 97.111
IKW40N120CS6 | 92.734 | 96.117 | 96.475 | 96.533 | 96.434 | 96.295 | 96.022
IKQ40N120CH3 | 93.641 | 96.432 | 96.725 | 96.717 | 96.614 | 96.422 | 96.235
How does new discrete IGBT7 compare to predecessor generations
Lower temperature
Higher efficiency
Higher power output
Chart: Max temperature in °C
| IKW40N120CH7 | IKQ40N120CH3 | IKW40N120CS6
 | 109.6 | 122.2 | 128.1
20°C
13°C
1.2%
G
C
E

## Slide 39: Maximum efficiency with 4-pin solution

## Slide 40: Difference – 3-pin vs. 4-pin
How does this influence anything?
G
C
E
G
C
E
K
Chart: Switching event 3-pin vs. 4-pin @ T = 150 [°C] V = 600 [V] Rg = 10.1 [Ω] Vg = 15 [V]
Controllability
Lower turn-on losses
Lower junction temperature
Power loop
+
Control loop
108 A/ns
0.8 A/ns
Chart: Turn on losses 3-pin vs. 4-pin @ T = 150 [°C] V = 600 [V] Rg = 10.1 [Ω] Vg = 15 [V]
| 4 | 10 | 20 | 40 | 80
IKZA40N120CS7 | 0.000644 | 0.001113 | 0.001786 | 0.002921 | 0.005837
IKW40N120CS7 | 0.0007415 | 0.00133 | 0.002337 | 0.004601 | 0.01229
Appnote 3pin vs 4 pin
E =
Notes: With 4 pin you benefit much compared to the 3 pin for eg. With lower the rg and higher the current the system losses will be lower

## Slide 41: Product and application benefits: IKW40N120CH7 vs IKZA40N120CH7
Chart: Efficiency vs. Temp
| 0.48399999999999999 | 1.179 | 1.639 | 2.3239999999999998 | 2.7789999999999999 | 3.23 | 3.6829999999999998 | 4.3540000000000001
IKZA40N120CH7 | 95.54 | 97.51 | 97.745 | 97.771 | 97.722 | 97.623 | 97.495 | 97.285
Competitor | 95.122 | 97.34 | 97.564 | 97.614 | 97.554 | 97.347 | 97.149
 | 41.6 | 50.5 | 56.3 | 69.8 | 78.8 | 86.9 | 97 | 111.8
 | 46.9 | 56.2 | 65.1 | 77.1 | 87.8 | 98.2 | 107.9 | 126
4-Pin
3-Pin
~ 30% lower losses
~ 19% lower case temperature
~ 17% more output current
~ 30% dv/dt or di/dt
IGBT7 is faster compared to previous generations.
The 4-pin devices are suggested to have better controllability and to
achieve higher dv/dt or di/dt.

The test conditions
Iout= 20 Arms, Vout = 230VRMS, Vin = 800V, Fpwm = 33.3 kHz, Pout = 4kW, Tj=130°C, Rg(on/off) = 10 ohm
0.1%
15°C
G
C
E
G
C
E
K

## Slide 42: System cost – „Affordability“
Notes: Include ePA measurement

## Slide 43: IGBT7: The cost-effective alternative to wide-bandgap solutions
Discrete IGBT7 is
bridging the gap between traditional silicon IGBTs and offering a cost-effective alternative to wide-bandgap solutions
System cost
Wide-bandgap
Performance
2007-2012
Highspeed 3
TRENCHSTOP™ performance
Older discrete silicon technologies
TRENCHSTOP™
TRENCHSTOP™ 2
TRENCHSTOP™ 5
TRENCHSTOP™ IGBT 6
2021-2025
61 products
2016 – Gen1
2024 – Gen2
Notes: "Get the best of both worlds with IGBT7 - combining the reliability of traditional Silicon IGBTs with the efficiency of widebandgap solutions."
"Experience the power of innovation with IGBT7 - the perfect solution for modern power designs."
"Step up your power game with IGBT7 - the future of efficiency and cost-effectiveness."
"Say goodbye to trade-offs with IGBT7 - the ultimate solution for high-performance power designs."
"Choose IGBT7 for superior power performance at an affordable price point - bridging the gap in today's power market."

## Slide 44: 1200 V IGBT7 vs. SiC MOSFET positioning
Chart: IvF Chart
| 10 | 20 | 30 | 40 | 50 | 75 | 100
1200V IKZA40N120CH7, 1X | 34.6 | 29 | 23.4 | 19 | 15.6 | 10.1 | 6.83
1200V IMZ120R060M1H CoolSiC, 1X | 19.73 | 19.56 | 19.4 | 19.245 | 19.07 | 18.15 | 17.2
1200V IKZA40N120CH7, 1X | 0.98088 | 0.97656 | 0.97177 | 0.96581 | 0.95864 | 0.9363 | 0.90754
1200V IMZ120R060M1H CoolSiC, 1X | 0.97989 | 0.97912 | 0.97831 | 0.97746 | 0.97663 | 0.97559 | 0.97456
40 kHz
SiC MOSFET
both
IGBT
20 kHz
CoolSiCTM MOSFET
TRENCHSTOPTM IGBT7 H7
Discrete IGBT7 is
bridging the gap between traditional silicon IGBTs and offering a cost-effective alternative to wide-bandgap solutions
Efficiency
Out Current
CoolSiCTM MOSFET
TRENCHSTOPTM IGBT7 H7

## Slide 45: Quality – „Robustness“
Notes: Include ePA measurement

## Slide 46: Quality requirement discretes
The robustness validation stess times
What
  High voltage – high humidity high-temperature reverse bias storage
  Hard failure of the devices and blocking voltage drifts down over time
Why?
  Corrosions at field plates
  Corrosion of DLC film
  Delamination in the passive layer
  Corrosion at contacts
only
High Voltage at High Humidity
Suitable for outdoor applications
  Solar
  Industry air-conditions
  Pump drives
  etc.
Certified by JEDEC standard for HV-H3TRB
JEDEC (Joint Electron Device Engineering Council)
Improved Edge Termination
Notes: Why this are the failures that can happen
it is Humidity robust device and has enhanced cosmic ray robustness. It is the first time we´ve ever promote something like this. This is a key value differentiator from the competition on this topic. It is a new ring that goes around, basically humidity robustness if often effecting, it is like a junction between an isolation ring and active cell, but here sometimes short is happening, so then the device can be destroyed, but now this edge for IGBT7 is much more (further improved) robust.
Which is very important as drives are working in harsh industrial environemnt

## Slide 47: Key takeaways and resources
5 values of discrete TRENCHSTOP™ IGBT7:
Easy to switch, fine controllability with a rugged transient
Advanced power density
Level up efficiency with silicon world
Optimized price/performance, with a global responsibility
Extra reliability, qualified for HV-H3TRB
3 voltage classes 650 V, 750 V & 1200 V
3 flavours T7, H7 & S7
7 packages
61 Products
Flexible family that suits the overall energy chain needs
IGBTs produced in a
newest fully-automated
300mm chip factory
infineon.com/discreteIGBT7

## Slide 48: Complementary products
&
Every switch needs a driver
EiveDRIVERTM
TRENCHSTOPTM IGBT7 modules
Notes: Goes hand in hand with Infineon gatedrivers